## Slide 1: Internet of Things using .NET
Using Raspberry PI and Mono C# to build an IoT device.

## Slide 2: Chris Berthold
Over 15 years of development experience developing quality software and network administration
10 years of business development in a manufacturing setting
6 years of development as software consultant
Private pilot
Currently works on the awesome Product Development Team for Flightdocs

## Slide 3
Cisco IBSG 2011 Infographic

## Slide 4
Cisco IBSG 2011 Infographic

## Slide 5: Introducing Raspberry Pi 2
The Raspberry Pi is a series of credit card-sized single-board computers developed in the UK by the Raspberry Pi Foundation with the intention of promoting the teaching of basic computer science in schools.
Because it has an ARMv7 processor, it can run the full range of ARM GNU/Linux distributions, including Snappy Ubuntu Core, as well as Microsoft Windows 10 (see the blog for more information)

## Slide 6: Building The Platform
NOOBS Installation

## Slide 7: Raspberry Pi 2

## Slide 8: Features and Specifications
A 900MHz quad-core ARM Cortex-A7 CPU
1GB RAM
4 USB ports
40 GPIO pins
Full HDMI port
Ethernet port
Combined 3.5mm audio jack and composite video
Camera interface (CSI)
Display interface (DSI)
Micro SD card slot
VideoCore IV 3D graphics core

## Slide 9: What you need to get started
A MicroUSB Power supply capable of 1.5Amps (2 amps suggested) – Samsung Galaxy S5 for example
A MicroSD card compatible with Raspberry PI 2
  Not all cards are created equal
  Recommend the NOOBS cards – great place to start and no issues
A TV with HDMI to plug into or a USB to TTL Serial Cable
A WIFI Dongle or Ethernet Cable for internet access

## Slide 10: What is Internet of Things?
The Internet of Things (IoT) is the network of physical objects or "things" embedded with electronics, software, sensors and connectivity to enable it to achieve greater value and service by exchanging data with the manufacturer, operator and/or other connected devices. Each thing is uniquely identifiable through its embedded computing system but is able to interoperate within the existing Internet infrastructure.

## Slide 12: In ENGLISH Please!
Alarm Activated
Toilet Bowl Cleaner Empty
Snooze Pressed

## Slide 13: Internet of Things: Operations
Input
Encode
Orchestrate
Encode
Output
Events
Events

## Slide 14: Types of Input and Output
Analog – A continuous signal for which the time varying feature (variable) of the signal is a representation of some other time varying quantity.
  Audio – Voltage varies with sound waves
  Pressure – Aneroid barometer uses rotary position
Digital – Finite number of values or steps (usually defined as exact voltage values)
  Switch – On/Off
  Gear Shifter – Park/Netural/Reverse/1/2/3
Encoded – Device, circuit, transducer, software, algorithm or person that converts information from one format or code to another, for purposes of standardization, speed, secrecy, or compressions
  Morse Code, Enigma
  BlueTooth Sound
  Web Services

## Slide 15: Inputs
Analog
  Microphone
  Temperature Sensors
  CO2 Sensors
  Radio Signal
Digital
  Relay
  Switch
  GPIO – General Purpose Input Output
Encoded
  BlueTooth Device
  Web Service
  Serial Device
  USB Device
  Inter-Integrated Circuit (I2C) Device

## Slide 16: Outputs
Analog
  Speakers
  Light Bulb
  Radio Signal
Digital
  Relay
  Multi Position Switch
  PWM – Pulse Wave Modulation
    Motors
    Actuators
Encoded
  BlueTooth Device
  Web Service
  Serial Device
  USB Device
  Inter-Integrated Circuit (I2C) Device

## Slide 17: Example of Direct IO in C#
Hello world Blinky LED Light

## Slide 18: GPIO PinOut

## Slide 19: Using a Shield with Raspberry Pi
GPS Shield
Serial Shield
Relay Shield

## Slide 20: GPS Signal to ForeFlight
Raspberry Pi 2
GPS Shield
+
Mono C#
Network Broadcast

## Slide 21: What will it do?
INPUT
  GPS Module
  gpsd
    Encoded to NMEA GPS encoding
    TCP localhost
      Port 2947
Output
  UDP Broadcast
    ForeFlight Encoded format
    Xxx.xxx.xxx.255
      Port 49002
C# application
  Orchestrates the inputs
  Converts data
  Responds to changes in position
  Outputs response on regular 1 second interval according to ForeFlight API
  Uses Reactive Extensions and Spatial.NET to create events for input and output

## Slide 22: Wrapping up – Q & A
Getting time for beer but always glad to field questions
Hope you enjoyed the presentation
If you think I’m going to write at least one more bullet point you may be right
I can fit more you know……
OK last one, have a good night, Thanks for coming!